## Slide 1
Cereal Grain Data Acquisition Device
Team Members: Ryan Donahue & Kennedy Caisley
Advisor & Client: Dr. Daniel Robertson

## Slide 2: Target Platforms

## Slide 3: Current Data Acquisition Devices
Expensive (>$600 per unit)
Difficult Assembly (20+ hours)
Unreliable
  Mechanical button failures
  Messy wires
  No protection features
Not User Friendly
  Poor navigation/user input
Poor performing hardware/software
INSERT IMAGES OF OLD DEVICES

## Slide 4: CropTop v2.0

## Slide 5: Microcontroller
Microchip PIC32MX795F512L
80MHz, 32-bit
USB, SPI, I2C, ADCs, PWM
Low-Cost
Familiar

## Slide 6: User Interface
7” 800x600 TFT LCD
  Resistive Touch Panel
FTDI FT812 Graphics Coprocessor
SPI Interface with PIC32 MCU
Slotted PCB
+
Ft812

## Slide 7: Load Cell Interface
Analog Devices AD7799
  24-bit ΔΣ ADC
  470Hz Sampling Rate
Supports up to 3 load cells
SPI Interface with MCU
Low-noise design
x3

## Slide 8: Motor Control
DC & Stepper Motor
  Up to ~4 Amps
DRV8872 & DRV825
Auxiliary Battery Support
Protection Schemes

## Slide 9: Rotation, Distance, Extension Measurement
All use PIC32 Hardware
Overcurrent/ESD Protection
Linear poten

## Slide 10: Data Storage
uSD Card Interface
  SPI Interface with MCU
USB 2.0 Port
Hot Pluggable
ESD/Overcurrent Protection
USB port also supports bar
code scanner
uSD card, and barcode scanner

## Slide 11: Temp, Humidity, Tilt, Time, Date, & Location
uBlox M8C GNSS Module
ST LIS3D Accelerometer
Silicon Labs Si7006 temp.
and humidity sensor
Infrequent access
  One shared I2C Interface
All three chps

## Slide 12: Software Design
Created Custom Development Board
  In-Circuit Programming
Github used for version control
All user code compiled to PIC32
  “Bare-metal”
Created software stack

## Slide 13: Software Stack
“Bottom-Up”
Development Style

## Slide 14: Mechanical Design
Mounts to TFT LCD
  3mm screws/standoffs
Board edge connectors
  Accessible thru holes in case

## Slide 15: Manufacturing Plan
Contract Manufacturer
  PCB and Assembly
Based out of Austin, TX
3 Week Lead Times
Low Per-Unit Cost

## Slide 16: Design Outcomes
A single printed circuit board
$150 per board
Zero assembly time
Improved user interface
Improved reliability
Smaller form factor
High performance
Straightforward codebase

## Slide 17: Question(s)

## Slide 18: CropTop v2.0